## Slide 1: MNA in Deterministic Networks
July 6, 2023

## Slide 2: Deterministic Networking
Provides a capability to carry specified unicast or multicast data flows for real-time applications with extremely low data loss rates and bounded latency within a network domain.
Techniques used include:
  reserving data-plane resources for individual (or aggregated) DetNet flows (including for active and hybrid OAM) in some or all of the intermediate nodes along the path of the flow
  providing explicit routes for DetNet flows that do not immediately change with the network topology
  distributing data from DetNet flow packets over time and/or space to ensure delivery of each packet's data despite the loss of a path (Packet Replication, Duplicate Elimination, and Order Preservation Functions (PREOF)

## Slide 3: Deterministic Network over MPLS
DetNet with MPLS data plane uses PW and MPLS-TE encapsulations and mechanisms
In fact, DetNet over MPLS is an example of Post-Stack Header (PSH)
F-Label(s) support DetNet forwarding sub-layer
S-Label and d-CW support DetNet service sub-layer, e.g., PREOF
d-CW conforms to the Generic PW MPLS Control Word defined in RFC 4385
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0 0 0 0| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 4: DetNet MPLS OAM
d-ACH identifies that the payload is not a DetNet data packet, For example, an OAM packet
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0 0 0 1|Version|Sequence Number| Channel Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Node ID |Level| Flags |Ses.ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 5: DetNet MPLS Aggregation
The DetNet data plane allows for the aggregation of DetNet flows to improved scaling. Because of the per flow resource allocation requirement of DetNet aggregation of flows is essential for scalability. Aggregation is achieved by using multiple label stacks, where an aggregate PW contains the individual DetNet flow's [RFC 8964, Figure 6.]. Inserting post stack data by MNA nodes in such DetNet aggregates breaks aggregation/de-aggregation functionalities of DetNet.
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|DetNet Flow Payload Packet |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| d-CW |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| S-Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| F-Label(s) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| d-CW |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| A-Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| F-Label(s) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Data Link |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Physical |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 6: DetNet MPLS and MNA
The use of ISD MNA in DetNet MPLS can be well-controlled, reserving additional resources for DetNet flow to which ISD MNA is applied
The use of PSD MNA might not only require additional resources but introduce processing overhead in DetNet Relay nodes (source and/or destination nodes in the DetNet service sub-layer)
Possible ambiguity encoding post-stack. Would PSD MNA precede, for example, d-CW or d-CW precede PSD MNA?

## Slide 7
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ---
|0 0 0 0| Sequence Number | d-CW
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ---
|N N N N|Version| PS-MNA-LEN | TYPE = POST-STACK-MNA | PS
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ MNA
~ Ancillary Data ~ HDR
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ---
~ Payload ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ---
|N N N N|Version| PS-MNA-LEN | TYPE = POST-STACK-MNA | PS
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ MNA
~ Ancillary Data ~ HDR
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ---
|0 0 0 0| Sequence Number | d-CW
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ---
~ Payload ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 8: Questions?
Thank you!